LOCK MAINTENANCE

All locks used by POM are engineered and constructed to provide years of trouble-free service.  Locks, like any other mechanism, will require some service in order to perform smoothly under high-use and extreme weather conditions.  POM, along with the manufacturers of the locks, recommends the following lubricants be applied approximately every six months to optimize lock performance.

- Changematic, Ace, and National tubular locks require lubrication with LPS-TKX, WD-40 (only non-lithium version), or Tri-Flow.  Customers will need to buy these from authorized local dealers or authorized Hazmat shippers – POM cannot ship them.

- Illinois Duo recommends LPS #01128 for lubricating its locks.  This has been found most stable under extreme cold conditions.  Again, this must be obtained directly from LPS or an authorized distributor.

- The Medeco, POM E-locks, and POM locks (POM, KXM, MCM, DPM, etc) should be lubricated using Lockease liquid graphite (POM #100-797), which can be purchased and shipped from POM.  If there is an excessive accumulation of foreign matter, we recommend first flushing the lock with a fast evaporating, non-residual spray such as MaxKleen Lectro-Solv.   Since these items are classified Hazmat, they must be purchased direct from local distributors.  If you can find a #111 degreaser, that will be the most effective.  After flushing out with the degreaser, you will need to re-lubricate the locks with Lockease.

- It is important to avoid the use of worn keys, so check them regularly for wear.  A dirty or improperly lubricated lock will show abnormal wear on the keys and premature breakage.  Continued use of a worn key will cause eventual damage to lock tumblers, and it is much cheaper to replace a key than all the locks it will damage when worn.  Note:  When installing a lock, always insert and hold the key when tightening the cam lock nut or screw.  Tumbler damage may otherwise result from the rotating force when tightening.

Revised 10/22/15