Insert the flat washer and Grade 5 bolt inside the meter vault, with the bolt extending out the bottom.   As you can see, the nut goes on the bolt with the flat side up.  Hook the three wedges on the nut as shown, and you should hold them on with a rubber band or they will fall off and go down inside the pipe while you are trying to set the meter on the pipe.    Set the meter on the pipe with the wedges inside, face it in the desired direction, and tighten the bolt.  The wedges will spread out inside the pipe.  You may have to come back in a few days and tighten the bolts, since they can actually stretch a little and make the meter seem loose in a few months.